## Slide 1: DEVELOPMENT OF USER INTERACTIVE SOFTWARE ‘INTER-PACK’ FOR FOOD PACKAGING SYSTEM DESIGN
UNDER GUIDANCE OF: ABHIJEET SINGH
Prof. S.K. DAS 09AG3208

## Slide 2: introduction
The principal roles of packaging are to contain, protect/preserve food and inform the user.
Keeping the contents clean, fresh, sterile and safe for the intended shelf life is a primary function.
It is therefore important for us to know for how much time the food material will remain stable and safe for consumption.

## Slide 3: objectives
To pool the database of packaging material, GAB constants for food material, bulk density of food material, price of packaging material
To use this database to design food packaging system using a user-interactive program

## Slide 4: REVIEW OF LITERATURE Food stability
The aim is to increase the shelf life keeping the cost of packaging in mind. Growth of microorganisms is influenced by the moisture content of the food material.
Water activity is an important consideration for food product design and food safety
The variation of water activity with moisture content of the food samples is thus important from a food safety perspective. This is modelled with the help of moisture adsorption isotherms.
There are certain models equations to mathematically relate the water activity and relative humidity.

## Slide 5: Water activity
It is defined as the vapour pressure of a liquid divided by that of pure water at the same temperature.
  where p is the vapour pressure of water in the substance, and p₀ is the vapour pressure of pure water at the same temperature.

## Slide 6: Moisture sorption isotherm
At equilibrium, the relationship between water content and equilibrium humidity of a material can be displayed graphically by a curve, the so called moisture sorption isotherm
For each humidity value, a sorption isotherm indicates the corresponding water content value at a given, constant temperature. If the composition or quality of the material changes, then its sorption behaviour also changes

## Slide 8: Gab model
The sorption isotherms of biological and food materials are mostly of sigmoid shape. The GAB model is considered one of the most useful ones which in many simple sorption cases can be used for the approximation of the experimental data at water activity of up to 0.9
m = moisture content (d.b)
aw = water activity
m0, c, K = three sorption parameters characterising the sorption properties of the materials .

## Slide 9: Diffusion of gases in solids
is the pressure gradient, kPa
is the permeability of the material, m3(STP) mm/ Pa m2s
z2-z1 is the thickness through which the gas diffuses, mm

## Slide 10: Multilayer diffusion
= Pressure gradient, kPa
Pi = Water vapour permeability of ith layer, m3(STP) mm/ Pa m2s
Li = thickness of ith layer, mm

## Slide 11: What the program does
It calculates the shelf life of the food material on the basis of GAB model taking into account the permeability of packaging material and storage conditions
It calculates the cost of packaging

## Slide 12: Need for such a software
The program is user friendly and interactive
The user interface allows for easy entering of data and viewing of the
output
It helps in the decision making process
As the values of time and cost are available the user can better make
the decision whether to choose that material or he/she wants to
change.
It gives a n estimate of the shelf life and cost quickly which would otherwise be tedious to calculate
We can easily vary the input parameters and see how they affect the shelf life and cost i.e. simulation can be done
It is portable means it can be carried and used in most systems and does not need to be installed.

## Slide 13: MATERIALS AND METHOD Packaging material database
Different packaging materials have different values of water vapour permeability. The choice of packaging material can significantly increase the shelf life
For different packaging material a database of permeability values and the price is maintained in a text fie as ‘watervapourpermeability.txt’

## Slide 14: Food material database
The food material database consists of m0, c, k values of the food material to be used in GAB equation.
The database is maintained in a text file: ‘gab_parameters.txt’. It can be updated as and when required by the user
‘Inter-pak’ also uses bulk density of the food material during calculations. The values of bulk density of food materials are maintained in a separate text file: ‘bulk_density.txt’.

## Slide 15: Values entered by the user
Storage conditions
Material for packaging
Mass of the food sample
Moisture content of the food sample
Dimensions of the sample

## Slide 16: INPUTS
Program
Relative humidity
[user]
Moisture content of the sample
[user]
Storage Temperature
[user]
Mass of sample
[user]
Dimensions of the sample
[user]
Permeability and other data of packaging material
[Database]
GAB model constant for food sample
[Database]

## Slide 17
Program
Cost of packaging(Rs)
Shelf life(in days)

## Slide 19: Programming language used
Programming language used is Java. This language is used because of its wide support for building Graphical User Interface (GUI). The Swing toolkit is used for building GUI. For writing code, compiling, debugging NetBeans IDE (Integrated Development Environment) is used.
Another reason for used of Java is that it is supported on wide number of platforms. Hence ‘Inter-pak’ can be run on any machine without installing.

## Slide 20: updating the database(packaging material)
If the packaging material is not in the database the user can update it
A pop up box allows the user to enter the permeability value, price of material and density
The user entered values are updated in the text file

## Slide 21: Pop-up box for updating the packaging material database

## Slide 22: updating the database(food material)
If the food material is not in the database the user can update it
A pop up box allows the user to enter the Gab equation parameters and density of food sample.
The user entered values are updated in the gab parameters and bulk density text files

## Slide 23: Pop-up box for updating the food material database

## Slide 24: Changing thickness and Multi-layer option
User can change the thickness of the packaging material if he is not satisfied by the shelf life/cost.
User can enter the number of materials and then select the packaging materials.
Equivalent permeability can be calculated as
P=

## Slide 25: IF THE USER DOESN’T WANT TO KEEP THE SETTINGS

## Slide 26: ‘CHANGE THICKNESS’ OPTION SELECTED

## Slide 27: Pop-up box for changing the thickness of packaging material

## Slide 28: ‘MULTILAYER’ OPTION

## Slide 29: Variation of temperature
Initially the program was using a constant temperature during calculations.
However in reality temperature varies during the day. So to consider this we use a pulse variation of temperature .The temperature varies between the minimum and maximum values during the day.
If the user chooses to keep the temperature variable, a pop-up box will ask the user to enter the mean, max, min temperature of the day.

## Slide 30: Pop-up box for entering mean, max. and min. temperatures

## Slide 31: RESULTS AND DISCUSSION Test case(updating food material database)

## Slide 34: Databases before running the program

## Slide 35: Pop-up box for updating the database

## Slide 36: Databases after running the program

## Slide 37: Test case (updating packaging material database)

## Slide 39: Permeability database before running the program

## Slide 40: Values entered for updating

## Slide 41: The updated database

## Slide 42: TEST CASE(WITH ALL THE OPTIONS)

## Slide 45: Pop-up box with the shelf life and cost

## Slide 46: Dialog box asking the user

## Slide 47: The user selects the ‘change thickness’ option

## Slide 48: New shelf life and cost of packaging

## Slide 49: Dialog box asking the user

## Slide 50: multilayer option pop-up box and the values entered

## Slide 51: Recalculated values of shelf life and cost

## Slide 52: Pop-up box for the variable temperature option

## Slide 53: Recalculated values keeping the temperature variable

## Slide 54: discussion
Inter-pak’ gives reasonable results with some values but gives absurd results with some others when the relative humidity is too low or the packaging layer is too thick. This is because it converges to a constant value of water activity (aw) before the limit is reached. Hence we get an infinite loop, taking a long time to reach a water activity of 0.6.

## Slide 55: conclusion
We note that the storage conditions have a major impact on the shelf life of a food material. Also the choice of packaging material and number of layers also affect the shelf life. The triangular pulse variation should be taken into consideration for the variation of temperature during the day

## Slide 56: references
1. BLAHOVEC.J., YANNIOTIS S. (2010), ‘Gab’ generalised
equation as a basis for sorption spectral analysis. Czech J.
Food Sci., 28:345-354.
2. Coles Richard, McDowell Derek, ‘Food Packaging
Technology’ (2003), cRc press, Blackwell Publishing.
3. CRCnetBASE – Handbook of food properties, Second
edition http://www.crcnetbase.com/isbn/978-0-8493-5005-4
4. F. Prothon, L.M. Ahrne, ‘Application of the Guggenheim,
Anderson and De Boer model to correlate water activity
and moisture content during osmotic dehydration of apples ’ ,
Journal of Food Engineering 61 (2004) 467–470
5. Geankoplis Christie J. ‘Transport Processes and Unit
Operations’, Third Edition (1993), Prentice Hall International
6. George Wypych , Handbook Of polymers(2012) , Chem tree
Publishing Toronto